#	Chip name:	Chip ID:	Flash size, Kb	Ram size, Kb	Mac address:	Flash word size:	Info page:	Support USB:	Lock data size:	Comment:
1.	CC2530	0xA5	32, 64, 128, 256	8, 8, 8, 8	0x780E, 8	4	0x7800 - 0x8000	-	16	The primary IEEE address resides in info page and is read only. The secondary IEEE address, which is optional, is stored at the end of the flash in the last 8 bytes before the lock bits.
	CC2531	0xB5	128, 256	8, 8	0x780E, 8	4	0x7800 - 0x8000	●
	CC2533	0x95	32, 64, 96	4, 4, 6	0x780E, 8	4	0x7800 - 0x8000	-
	CC2540	0x8D	128, 256	8, 8	0x780C, 6	4	0x7800 - 0x8000	●
2.	CC2430	0x85	32, 64, 128	8	0xDF43, 8	4	2Kb, special flash	-	1	IEEE address is stored in the last 8 bytes of the flash
	CC2431	0x89	32, 64, 128	8	0xDF43, 8	4		-
3.	CC2510	0x81	8, 16, 32	1, 2, 4	-	2	1Kb, special flash	-	1
	CC2511	0x91	8, 16, 32	1, 2, 4	-	2		●
4.	CC1110	0x01	8, 16, 32	1, 2, 4	-	2	1Kb, special flash	-	1
	CC1111	0x11	8, 16, 32	1, 2, 4	-	2		●
	CC430									Not supported by CC Debugger
	CC1010									Not supported by CC Debugger